Thermocouple with plug（TM2201)

Applications：

Analytical instruments, mechanical equipments, plastic processing machineries, heaters, petrochemical devices.

Technical data:

Connecting cable:  Shielded compensating cable

Protection tube:    Stainless steel 304

Sensor element:    Thermocouple

接线图-wiring diagram

红-red 白-white

Dimensions（外形尺寸图）

Order Details:

| TM2201 | — | (1) | — | (2) | — | 000 | — | (4) | — | 00 | — | (6) | / | (7) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

- Protection tube diameter D

05       0.5mm

10       1.0mm

15       1.5mm

16       1.6mm

20       2.0mm

- Insertion length  EL

150     150mm

300     300mm

500     500mm

1000    1000mm

2000    2000mm

- Sensor element

OE        Type E Thermocouple

OK        Type K Thermocouple

OJ         Type J Thermocouple

OL        Type L Thermocouple

OS        Type S Thermocouple

OT        Type T Thermocouple

OR        Type R Thermocouple

- Cable length  L（L≥100mm）

100     100mm

200     200mm

2000    2000mm

(100≤L<1000 ,L1=50, L≥1000, L1=100)

Note: other lengths as per customers’ requirement.

- Additional options

00      No

01      strain relief spring/strain relief spring hose

03      Waterproof function

07      Ferrules as per DIN 46 228 part4 (Standard)

08      Multipole connector(providing type)

99      Special Options

List the additional options in sequence, separated by commas.